## Slide 1: Optimisation at Wairakei AKA “Optimising the well operation and steamfield configuration tracking tool at the Wairakei geothermal system”
Vida Fox
Logan Wu
Image: https://www.vectorstock.com/royalty-free-vector/geothermal-energy-concept-eco-friendly-geothermal-vector-19426193

## Slide 2: Introduction to Wairakei
70 Wells
10 Flash Plants
4 Power Plants
3 steam powered
1 water powered
Notes: A standard commercial geothermal field has three main components:
wells , flash plants, power plants - use steam used to turn turbines that drive generators to produce electricity.
At the Wairakei steam field, owned and operated by contact energy, there is a complex network of approximately 70 wells, that feed fluid to >10 flash plants and 4 power plants (3 steam, 1 water powered/binary). //

## Slide 3: Binary Plant
Water
Heat exchanger
Pentane
Turbine
Notes: -> The water powered plant is called a binary plant. This harnesses energy from hot separated water by using it to heat and evaporate pentane in a closed system. Once in a gaseous form the pentane turns turbines to generate electricity in the same way as steam, before being cooled and recycled.//

## Slide 4: Steamfield Network
1
...
2
...
...
n
FP1
FP2
steam & water
Power Plant 1
Power Plant 2
steam
Binary Plant
water
water
reinjection, prawn farm, etc
steam
Notes: These three key components, wells, FPs and PPs naturally form a simple network (pictured). Each FP feeds fluid to a specific power plant, however there are a selection of wells that are able to be directed to different FPs at different times. These are called swinging wells and are shown in this diagram by wells with 2 arcs, (a solid active arc and a dashed inactive arc).
As well as this, each of the power plants produces electricity from steam, or water, at different rates. And the binary plant can only take water from certain flash plants. For these reasons there is the opportunity to optimise well configuration, to maximise electricity production.//

## Slide 5: Current System
Well
FP
Gen
Data & Workbooks
Operator
Field Team
Notes: Currently decisions concerning well configuration are made using data in a series of Excel workbooks. It is quite a manual process based on rules of thumb, and staff expertise.
This poses a number of challenges; there is no guaranteed optimality, the spreadsheets are slow, there is a lack of transparency, and data values are prone to a margin of error.//

## Slide 6: Project Division
Vida | Logan
Integer programming Decision optimisation | Bayesian simulation Uncertainty
Image: https://commons.wikimedia.org/wiki/File:Max_paraboloid.svg
Notes: Our solution to these challenges has two parts. I created a mixed integer linear program to optimise the configuration of a subset of the Wairakei steam field. And Logan has used Bayesian modelling to take into account uncertainty in our data and parameter values.

## Slide 7: Optimisation
Subset of Steamfield network:
35 wells - mass flow, enthalpy.
4 flash plants (FP) - pressure, enthalpy of water/steam.
4 power plants - efficiency factor (gives MW).
Assumptions:
Independence - rest of steam field doesn’t affect this region.
Measurements/data are accurate at given time.
Notes: To create my mixed integer linear program, I used a subset of the steam field. This subset contains 35 wells, 4 FPs and all PPs at Wairakei. Within this is all swinging wells, and hence all wells where decisions can be made for the steamfield configuration.
Several assumptions have to be made to model this system, the key ones being that the state of the rest of the steamfield doesn’t affect this region, and that the values used are accurate at the given time.
The important data values needed to model this system are: the mass flow and enthalpy of the fluid coming out of each well, the pressures in each flash plant and the enthalpy of water and steam at those pressures, and the efficiency factor of each power plant. These values, all provided to us by Contact Energy, allow us to calculate the amount of steam or water going into each power plant, and convert this to a number of MW generated.//

## Slide 8: Steamfield Network
1
...
2
...
...
n
FP1
FP2
steam & water
Power Plant 1
Power Plant 2
steam
Binary Plant
water
water
reinjection, prawn farm, etc
steam
Notes: The goal of this model is to choose an optimal configuration of swinging wells to maximise electricity production. Previously, I showed you this network diagram, now let’s look at this for a single well.

## Slide 9: Steamfield Network
Well
FP1
FP2
steam & water
Power Plant 1
Power Plant 2
steam
Binary Plant
water
water
steam
steam & water
reinjection, prawn farm, etc.
Notes: We want to decide whether to swing this well to FP1 or FP2.//

## Slide 10: Steamfield Network
Well
FP1
FP2
steam & water
Power Plant 1
Power Plant 2
steam
Binary Plant
water
water
steam
steam & water
reinjection, prawn farm, etc.
Notes: If we swing it to FP1, making this arc active, we can use both its water and steam to produce electricity because FP1 connects to the Binary Plant. //

## Slide 11: Steamfield Network
Well
FP1
FP2
steam & water
Power Plant 1
Power Plant 2
steam
Binary Plant
water
water
steam
steam & water
reinjection, prawn farm, etc.
Notes: But, FP2 goes to PP2 which may produce electricity from steam at a higher rate.//

## Slide 12: Steamfield Network
Proportions of steam and water depend on enthalpy.
Well
FP1
FP2
steam & water
Power Plant 1
Power Plant 2
steam
Binary Plant
water
water
steam
steam & water
reinjection, prawn farm, etc.
Notes: Now this well, might have high or low enthalpy, where a higher enthalpy means its fluid will contain a larger proportion of steam, so we might chose to swing the well to FP2, where steam goes on to the more efficient steam powered plant. //

## Slide 13: Steamfield Network
Well
FP1
FP2
steam & water
Power Plant 1
Power Plant 2
steam
Binary Plant
water
water
steam
steam & water
reinjection, prawn farm, etc.
Different Pressures
Notes: Each FP operates at a different pressure, which also affects the amount of steam that gets sent into the power plants. These are all factors included in my model.//

## Slide 14: Decision Variables
Well
FP1
FP2
steam & water
Power Plant 1
Power Plant 2
steam
Binary Plant
water
water
steam
steam & water
reinjection, prawn farm, etc.
2 Decision Variables for each arc:
- binary variable ∈ {0,1}
- continuous variable ∈ (0,1)
Notes: This swinging well decision is represented by a pair of decision variables for each arc. A binary decision variable and a continuous decision variable. The binary variable represents whether or not a given arc is active, that is whether the flow from the well is swung to a given FP. The continuous variable is between 0 and 1 and represents the percentage of the mass flow of the well that is allowed to flow (throttling).//

## Slide 15: Objective Function
Well
FP1
FP2
steam & water
Power Plant 1
Power Plant 2
steam
Binary Plant
water
water
steam
steam & water
reinjection, prawn farm, etc.
MW produced = Sum of steam/water into each power plant divided by the efficiency factor for the given power plant
Notes: The Objective Function here is to maximise the number of MW of power produced by the steamfield. This is calculated as the sum of the steam/water into each power plant divided by the efficiency factor for that plant.

## Slide 16: Constraints
Well
FP1
FP2
steam & water
Power Plant 1
Power Plant 2
steam
Binary Plant
water
water
steam
steam & water
reinjection, prawn farm, etc.
Notes: I have used 4 constraints for my model, I consider these the main constraints on the system though there are numerous others that could be included.

## Slide 17: Constraints
Well
FP1
FP2
steam & water
Power Plant 1
Power Plant 2
steam
Binary Plant
water
water
steam
steam & water
reinjection, prawn farm, etc.
3 Constraints:
- One active arc per well
- Flow along active arc ⩽100%
- Flow along active arc ⩾
specified minimum flow
Notes: There are 3 constraints relating to the arcs between wells and FPs.
The first is that a maximum of one arc from each well can be active, that is, a well can only be connected to one FP at a time.
The second ensures that flow along an active arc is less than 100% of the full capacity mass flow of the well.
The third allows the user of this model to set a minimum flow for all or some of the wells.

## Slide 18: Constraints
Well
FP1
FP2
steam & water
Power Plant 1
Power Plant 2
steam
Binary Plant
water
water
steam
steam & water
reinjection, prawn farm, etc.
- Conservation of Mass
- Sum of steam into FPs ⩽ steam
flow limit of FPs
Notes: Finally, each flash plant has an operational limit on the amount of steam that can pass through it, this gives us our fourth constraint that the sum of the steam flow out of each FP must be lower than this limit.

## Slide 19: Subset Network
Notes: The culmination of decision variables, constraints and the objective function, as I have described, was formulated and solved in Excel using OpenSolver.
The subset of the steamfield I modelled, with 35 wells, is represented on this diagram, where wells are numbered 1-35 and FPs labelled A-D.

## Slide 20: Subset Network
Notes: Each line leaving a well, like this one, is an arc in the network

## Slide 21: Subset Network
Notes: a well that can be swung to 2 FPs has 2 arcs

## Slide 22: Subset Network
Notes: and one that can be swung to 3 has 3.

## Slide 23: Actual Configuration - 1 Dec 2017
Active Arc
Inactive Arc
Notes: The data provided to us that I used for this model was for the 1 December 2017. On this day Contact was operating with this configuration.

## Slide 24: Optimised Configuration
Active Arc
Inactive Arc
Notes: When I solved my model, this was the optimal configuration. As you can see, very little has changed.

## Slide 25: Actual vs Optimised Configuration
Active Arc
Inactive Arc
Was Active
Notes: In fact, only three wells have been swung differently in the optimised configuration, wells 17, 19 and 33.

## Slide 26: Actual vs Optimised Configuration
More fluid to FP B & C.
FP B & C feed to more efficient power plants.
This maximises electricity produced.
May not be practical to operate so close to the FP steam limits.
The true configuration is very similar.
Notes: This makes sense because it results in more fluid going to FPB and C which connect on to the more efficient power-plants. However, this optimised configuration results in FPB and C operating at, or close too, their steam flow limits. It may not be practical to operate so close to the flash plant steam limits, hence there may be good reason for the less optimal true configuration.

## Slide 27: Results of LP
Actual Configuration - 279.5 MW.
Optimised configuration - 286.0 MW.
6.5 MW / 2.3% increase in electricity production.
⩾75% of average contribution of a well
Model could be a good tool to help steamfield configuration decisions.
279.5 MW actual
286 MW optimised
Total Power

## Slide 28: Future Work for LP
Expansion to whole steamfield.
  Allows inclusion of different constraints.
Expansion to include wastewater flows.
  Re-injection, river, other uses.
Simulate with many different sets of data.
Combine with Bayesian Modelling
Notes: There are a number of areas of potential future work for this model. It could be extended to the whole steamfield, which would allow additional constraints to be added such as maximum total mass take, or environmental constraints. The waste water network, where geothermal water is reinjected into the ground, sent to the Waikato river or held in ponds, could by modelled. Or we could run simulations with the model using many different sets of data and parameters, in order to understand the sensitivity of the steamfield.
As Logan will discuss later, this model could also be integrated with his Bayesian Model.
All of these options would further extend the capabilities of my model as a decision-making tool.
I will now hand you over to Logan to talk about Bayesian modelling.

## Slide 29: Simulation
Uncertainty and risk
Bayesian simulation
Measurements contain error
Parameters contain uncertainty
image: The Matrix (1999)

## Slide 30: Missing Data
Hierarchical model
Missing wells imputed from a distribution
Observed wells
Parameter distribution
Unobserved well

## Slide 31: Statistical Method
Bayesian simulation
Prior x Likelihood = Posterior
RJAGS

## Slide 32: Simulation Process
Wells

## Slide 33: Simulation Process
Physical transformations
Flash Plant
steam
water
mixed phase

## Slide 34: Simulation Process
Physical transformations
Generator
Steam
Water

## Slide 35: Full Network
~6000-dimensional

## Slide 36: Simulation Process
Simulate the posterior with Gibbs Sampling

## Slide 37: Simulation Results

## Slide 38: Simulation Results

## Slide 39: Simulation Results
Find probability of constraint violation
FP14
FP15
FP16
<0.01%
<0.01%
<0.01%

## Slide 40: Simulation Results

## Slide 41: Simulation Results

## Slide 42: Future Work
Integrate more data

## Slide 43: Future Work
Combine LP and Simulation
Compare top n LP policies
All possible policies
Top n policies
Ranked policies
Linear program
Stochastic simulation
?
?
?
1
2
3

## Slide 44: Future Work
Environmental constraints
Reinjection modelling and constraints
Soft constraints

## Slide 45: Limitations
Model only includes surface network, no subsurface interactions
Offline: not linked to production database
Sensitive to systematic error

## Slide 46: Conclusions
Two models
Contact’s configuration is similar to our optimisation
We implement uncertainty and risk estimates
Can always use more data

## Slide 47
Thank you
Questions?

## Slide 48: Steamfield Network
1
...
2
...
...
n
FP1
FP2
steam & water
Power Plant 1
Power Plant 2
steam
Binary Plant
water
water
reinjection, prawn farm, etc
steam
Notes: Decision - which wells to send where

## Slide 49: Bonus 1

## Slide 50: Mixed Integer Linear Program Formulation

## Slide 51: Mixed Integer Linear Program Formulation

## Slide 52: Simulation Results
“Filler” time-series wells

## Slide 53: Regression Diagnostics

## Slide 54: Time-series Comparison

## Slide 55: Diagnostics

## Slide 56: Linear Program of Steamfield
Decision Variables: Binary & non-binary for each arc
Objective Function - Maximise MW:
Sum of steam/water into each power plant ÷ by efficiency factor.
Constraints:
Number of active arcs from each well <=1 (each well to one FP).
Flow along an active arc is <=100% of full mass flow of well.
Sum of steam into each FP is less than steam limit of FP.
A minimum level of flow for wells, where specified.
Notes: too busy - break it up

## Slide 57: Constraints
1 Constraint:
- Sum of steam into FPs ⩽ steam
flow limit of FPs
3 Constraints:
- One active arc per well.
- Flow along active arc ⩽100%.
- Flow along active arc ⩾
specified minimum flow.
Notes: Decision - which wells to send where

## Slide 58: Results of LP
6.5 MW / 2.3% increase in electricity production.
⩾75% of average contribution of a well
Model could be a good tool to help steamfield configuration decisions.
279.5 MW actual
286 MW optimised
Total Power